TUG BOAT  ‘ SAMHO T-9 ’

| GENERAL |  |
| --- | --- |
| VESSEL’S NAME | SAM HO T-9 |
| BUILDER | NAM YANG SHPBUILDING CO., LTD |
| YEAR BUILT | 07th jan. 2011 |
| TYPE | TUG BOAT |
| CLASSIFICATION SOCIEAT | K.R |
| FLAG | KOREA |
| IMO NO /Official NO / Call Sign | 9618434 / BSR-110007 / DSQZ7 |
| NAVIGATION AREA | GREAT COASTAL |
| DIMENSIONS |  |
| LOA | 34.23 M |
| Breadth (MLD) | 10.00 M |
| Depth (MLD) | 4.50 M |
| GRT | 287.0 TON |
| NET TON |  |
| SPEED | 13.50 KTS |
| Tank Capacity |  |
| FO(B-A) | 145.0 m3 |
| MGO | 25.0 m3 |
| L.O | 10.00 m3 |
| Ballast Capacity | 20.00m3 |
| Fresh Water | 25.0 m3 |
| PERFORMANCE |  |
| E/R MACHINERY |  |
| MAIN ENGINE | 2,250 PS * 750RPM * 2 SET |
| ENGINE TYPE / MODEL | NIIGATA 6L28HX |
| F.O CONSUMPTION | 450 ℓ/ h |
| MAIN GENERATOR ENGINE | 250PS(168KW) * 1,800RPM * 2 SET |
| ENGINE TYPE / MODEL | AD086TIS / DOOSAN |
| D.O CONSUMPTION | 15 ℓ/ h |
| PORT GENERATOR ENGINE | 126PS(80KW) * 1,800RPM *1 SET |
| ENGINE TYPE / MODEL | AD136T / DOOSAN |
| D.O CONSUMPTION | 10 ℓ/ h |
| CLUTCH | - |
| PROPELLER | Z-PELLAR(NIIGATA ZP-31) / KORT |
| DECK MACHINERY |  |
| ROPE TOWING WINCH | 300M * 120￠ |
| WIRE TOWING WINCH | 700M * 50￠ |
| Communication |  |
| VHF(DSC) * 2SET | WEATHER FAX * 1SET |
| AIS * 1SET | INMARSAT-C(INCUL. LRIT) * 1SET |
| RADAR * 2SET | SSB / DSC * 1SET |
| EPIRB * 1SET | TWO-WAY VHF * 2SET |
| GPS PLOTER * 2SET | RADAR TRANSPONDER * 1SET |
| MAGNETIC COMPASS * 1SET | Echo Sounder/Speed Log *1SET |
| MF/HF(DSC, NBDP) * 1SET | FIRE DETECTOR * 1SET |

Particulars are given entirely without warranty as to correctness and interested parties must satisfy themselves by inspection of the vessel.

# Text boxes

MYUNG JIN SHIPPING CO., LTD.

RM. 801, MYUNGJIN BLDG., 183, HASINBEONYEONG-RO, SAHA-GU, BUSAN, KOREA